## Slide 1: Open Systems Interconnection (OSI) Model
Notes: The Open Systems Interconnection model (OSI model) is a conceptual model that characterizes and standardizes the communication functions of a telecommunication or computing system without regard to its underlying internal structure and technology. Its goal is the interoperability of diverse communication systems with standard communication protocols. The model partitions a communication system into abstraction layers. The original version of the model had seven layers.

## Slide 2: OSI Model
OSI model is made up of seven layers that comprise everything that is needed for reliable communication between computers
Basic Rules
  Similar functions are grouped together in the same layer
  Every layer is serviced by the layer beneath it and serves the layer above it. -- Important since every layer does its own communication, new developments in any one layer don't break any of the other ones.
  Every layer involved in communication from one computer communicates directly with the same layer on the other computer
Application
Presentation
Session
Transport
Network
Data Link
Physical Link
Application
Presentation
Session
Transport
Network
Notes: How were all these different systems going to talk? The answer was “wedge” a universal address system into existing networks, a system we generally call Internet Protocol (IP).
Think about it this way: imagine your friend overseas sends you a package. That package may travel by plane, train or automobile, but you don't really need to know the airline schedule or the location of the nearest train station. Your package will eventually arrive at your street address, which is ultimately the only thing that matters.
Your IP address is a lot like this: packets may travel as electrons, beams of light or radio waves, but those systems don't matter to you. All that matters is your IP address, and the IP address of the system with which you're talking.
One thing that complicates this idea in the real world is that more than one person may be living at a single address. In the networking world, that's what's happening when one server provides for instance both regular HTTP and secure HTTPS, as well as FTP. Notice the P at or near the end of those acronyms? That's always a dead giveaway for protocol, which is just another way of saying “a type of communication.”
This lesson will help you understand how protocols and their ports work in Windows, Linux, and OSX. You'll also become familiar with several utilities (some of which have already been introduced in the previous lesson) that explore your system's networking capabilities. At the end of the lesson you should have a basic knowledge of: • the concepts of networks and how communication takes place • IP addresses • ports and protocols

## Slide 3
A real-life story converted to networking: Postal Service
Reminder: You are unable to “skip” any layers of the OSI model. You always have to work your way through ALL layers.
7) You write a letter
6) You put the letter in an envelope
5) You write your name and the name of the receiver on the envelope.
4) You put the envelope in the mailbox
3) The content of the mailbox will go to the central processing office of the postal service
2) Your envelope will be delivered to the receiver
They open the envelope and read its contents
Going from the application layer all the way down to the physical layer is what we call encapsulation.
Going from the physical layer and working your way up to the application layer is called de-encapsulation.
Notes: 7) You write 1000 invitations for an event in a language that the Receiver can understand using a medium they can accept. The language and contents can vary per recipient.
6) You wrap the letters in an envelope that the Network can accept.
5) You write the Sender and Receiver address on the envelops in a way the Postal System will understand.
4) You separate the letters into bundles of 100 and drop in the mailbox. The mailbox records the envelop information and waits for a return receipt.
3) The letters are transported to the local Terminal Post Office and sorted into new bundles for transport to the next Post Office on route to the recipient. Routing information is added to the envelope to allow the Data Link Layer to move the letter to the right recipient.
2) Data Link Layer moves bundles / letters from Post Office to Post Office. Once they arrive at the final Post Office, they are ready for delivery.
1) The mail carrier delivers the letter and receives a receipt. This receipt is sent back to sender using the ‘Lower Layers’ of the stack until the Transport Layer receives the receipt. If the receipt is in order, were done. If not, the letter is received by level 4.
Once again, you are unable to “skip” any layers of the OSI model. You always have to work your way through ALL layers. If you want a real-life story converted to networking land just think about the postal service:
First, you write a letter.
You put the letter in an envelope.
You write your name and the name of the receiver on the envelope.
You put the envelope in the mailbox.
The content of the mailbox will go to the central processing office of the postal service.
Your envelope will be delivered to the receiver.
They open the envelope and read its contents.
If you put your letter directly in the mailbox it won’t be delivered. Unless someone at the postal office is friendly enough to deliver it anyway, in network-land it doesn’t work this way! Going from the application layer all the way down to the physical layer is what we call encapsulation. Going from the physical layer and working your way up to the application layer is called de-encapsulation.

## Slide 4: (1) Physical Layer
This layer defines the physical specifications of the devices and what needs to be done in order for the information to be transmitted over the selected medium.
Notes: For a WiFi connection, this is a radio signal; for a fiber connection it's the light being sent; or for a copper connection the electronic signal being sent on the wire.

## Slide 5: (2) Data Link Layer
The data link layer was designed to deal with ensuring the physical layer can recover from errors that might happen and to deal with different connecting mediums.
Basically it prepares (encapsulates) data so that it can be transmitted over whatever physical means are necessary (radio waves, fiber-optic cable, copper).

## Slide 6: (3) Network Layer
This layer is responsible for the addressing part of the connection.
Not only on ensuring that each address is unique on the network, but also on making sure that whatever path is available (whether a good or a bad one), it always delivers the information where it needs to go, and that our information will be sent from hop to hop until it reaches its final destination.

## Slide 7: (4) Transport Layer
Provides transparent transfer of data between computers, providing reliable data transfer services to the upper layers.
This means that it is responsible for assembling all data in smaller portions that can be carried reliably on a data network. If a packet is lost or not received, it is the transport layer's job to make sure that that single packet is retransmitted and then reassembled in the correct order.

## Slide 8: (5) Session Layer
Responsible for dialogue control between two computers. Basically it establishes, manages and terminates all connections that happen between the computers.

## Slide 9: (6) Presentation Layer
Responsible for guaranteeing that data is exchanged in a way that is comprehensible between both parties. In some services that use a form of encryption, the encryption happens at the presentation layer.

## Slide 10: (7) Application Layer
Responsible for direct interaction between applications and the user interface to the application, for instance the use of a web browser like IE or Firefox.

## Slide 11: Appendix

## Slide 12: Every layer involved in communication from one computer communicates directly with the same layer on the other computer
EXAMPLE:
When you type www.google.com in your browser, there is a direct interaction between your computer's Layer 7 interface (your web browser) and Google.com's web servers (also a Layer 7 interface).

## Slide 13: Networking Defined
A computer network consists of two or more computing devices that are connected in order to share the components of your network (its resources) and the information you store there, as shown. The most basic computer network (which consists of just two connected computers) can expand and become more usable when additional computers join and add their resources to those being shared.
Notes: The first computer, yours, is commonly referred to as your local computer. It is more likely to be used as a location where you do work, a workstation, than as a storage or controlling location, a server. As more and more computers are connected to a network and share their resources, the net- work becomes a more powerful tool, because employees using a network with more information and more capability are able to accomplish more through those added computers or additional resources. The real power of networking computers becomes apparent if you envi- sion your own network growing and then connecting it with other distinct networks, enabling communication and resource sharing across both net- works. That is, one network can be connected to another network and be- come a more powerful tool because of the greater resources. For example, you could connect the network you and your classmates develop for this course to similarly con- structed networks from other intro- ductory networking classes if you wanted them to share your infor- mation and networked resources. Those classes could be within your own school, or they could be anywhere in the world. Wherever that newly joined network is, the communication and resource shar- ing activities in that new network could then be shared with anyone connected to your network. All you have to do is join that new network’s community or allow its members to join yours. In addition, a company’s cost of doing business can be reduced as a result of sharing data (defined as a piece or pieces of information) and re- sources. Instead of having individual copies of the data at several locations around the company, and needing to keep all of them similarly updated, a company using a network can have just one shared copy of that data and share it, needing to keep only that one set of data updated. Furthermore, sharing networked resources (like printers) means that more people can use a particular resource and a wider variety of resources (like different printers) can be used by each network user. Any time a company can do more with less, or buy fewer items to do the same job, its total costs are reduced, and it is able to make more money per dollar spent.

## Slide 14: Information Sharing
A network is a collection of computers and devices connected together via communications devices and transmission media. Many businesses network their computers together to facilitate communications, share hardware, share data and information, share software, and transfer funds.
A network can be internal to an organization or span the world by connecting to the Internet. Instead of using the Internet or an internal network, some companies hire a value-added network provider for network functions. A value-added network (VAN) is a third-party business that provides networking services for a fee.
Networks facilitate communications among users and allow users to share resources with other users. Some examples of resources are data, information, hardware, and software
Networks are used for a number of reasons, one way or another it’s usually about sharing:
Information: we use networks for applications like e-mail or to reach certain websites.
File sharing: we need a network so that users can reach a shared network drive with documents, pictures and/or other files.
Resource sharing: we can connect a printer to the network that is used by multiple users. No need to connect a printer directly to each computer.
Application sharing: we might have users that require access to the same application. For example, a finance department with five users that need access to the same bookkeeping software.
Notes: Computers increase your ability to communicate. Once you begin working with a computer, you are likely to become more productive. However, what do you do with that increased productivity if you are not connected to any- one? Communication requires not only someone with information to share but also someone on the other end with whom to share it. Companies don’t benefit by creating sheer volumes of output—they benefit when the in- creased output helps them make better decisions or increases the likelihood of increased income. Having your computers networked allows you to do both with your newfound increases. The initial reason for developing most computer networks was to assist users with sharing their increased output, especially between computers in the same general vicinity, as shown in Figure 1.4. However, users wanted not only to share information with others, they wanted to communicate about that information after someone else had it, too. In addition to trans- mitting the user’s original information, computer networks enabled those users to discuss what was being transmitted, and this resulted in even more communication. Additional network communications techniques thus came into being, such as e-mail and video conferencing. Furthermore, with the increases in the sizes of networks, sharing no longer had to be concerned with proximity. The use of networks has effectively erased distance and time constraints. You can communicate almost instantly to anywhere in the world that is connected to your network.
Networks are an effective way to communicate. Using networks, companies can send the same information to large numbers of employees or customers quickly and efficiently. Examples include company newsletters and announcements for employees, as well as advertisements and purchase in- formation for customers. Also, individual employees are more likely to communicate with larger numbers of individuals both inside and outside the company using e-mail, an electronic means of communicating that is similar to mail but done on computers, usually over the Internet, over net- works. E-mail is the most commonly used feature of the Internet, and its use is growing dramatically. In fact, e-mail is fast becoming the primary choice for much of our daily communication.

## Slide 15: Network Communications Standards
Today’s networks connect terminals, devices, and computers from many different manufacturers across many types of networks, such as wide area, local area, and wireless. For the different devices on various types of networks to be able to communicate, the network must use similar techniques of moving data through the network from one application to another.
Many users opt for wireless transmission media because it is more convenient than installing cables. In addition, businesses use wireless transmission media in locations where it is impossible to install cables. Types of wireless transmission media used in communications include infrared, broadcast radio, cellular radio, microwaves, and communications satellites.

## Slide 16: Wi-Fi (Wireless Fidelity)
Wi-Fi is a series of network standards that specifies how two wireless devices communicate over the air with each other. Using Wi-Fi, computers or devices that have the appropriate wireless capability communicate via radio waves with other computers or devices. The Wi-Fi standard uses techniques similar to the Ethernet standard to specify how physically to configure a wireless network. Most of today’s computers and many personal mobile devices, such as smart phones and handheld game consoles, are Wi-Fi enabled.
One popular use of the Wi-Fi standard is in hot spots that offer mobile users the ability to connect to the Internet with their Wi-Fi enabled wireless computers and devices. Many homes and small businesses also use Wi-Fi to network computers and devices together wirelessly.

## Slide 17: Broadcast Radio Signals
Broadcast radio is a wireless transmission medium that distributes radio signals through the air over long distances such as between cities, regions, and countries and short distances such as within an office or home. Bluetooth, UWB, Wi-Fi, and WiMAX communications technologies discussed earlier in this chapter use broadcast radio signals.